## Slide 1: Sensors in Snowy Alpine Environments: Progress Report
Martha Apple*, James Gallagher†, Kevin Negus*, Samuel Croft*, Tyler Vendetti*, and Carson Fiechtner*
*Montana Tech, †OPeNDAP
<mapple@mtech.edu>, <jgallagher@opendap.org>

## Slide 2: Alpine plants act as sentinels of climate change.

## Slide 3: Overview
About Open Source Hardware
Our designs for an in-situ sensor network
LoRa Background
Test implementation

## Slide 4: Open Source Hardware
Closely aligned to the Open Source Software movement
  "Open hardware," or "open source hardware," refers to the design specifications of a physical object which are licensed in such a way that said object can be studied, modified, created, and distributed by anyone.1
A few companies that support OSH:
  Adafruit, SparkFun, Seeed, Mouser, OSHPark, …
Tools:
  Arduino (IDE, MCUs), Fritzing (CAD), GitHub, BitBucket (code repositories)
Umbrella organizations:
  OSHWA, opensource.com
1. https://opensource.com/resources/what-open-hardware

## Slide 5: Most Importantly…
Open Source Hardware provides an easy way to share ideas
And learn about techniques
So we can build devices we need that (may) lack mass-market appeal

## Slide 6: Overview
About Open Source Hardware
Our designs for an in-situ sensor network
LoRa Background
Test implementation

## Slide 7: Requirements
Soil temperature and moisture monitoring
Operation unattended in remote, harsh environments
Remote connectivity
Low cost

## Slide 8: Sensor Network: Basic Design
Deploy sensors at research sites (initial site: Goat Flat, ~9,000 ft).
Sensor nodes should run on battery power for 2+ years.
Use LoRa radio to connect sensor nodes to a master node.
Use the master node to forward data to the Internet.
The master node will use cell phone Satellite technology for an Internet uplink.
  Subsequent implementations could use other techniques.
Data from the master node will be sent to an Application Server that can be accessed from browsers and analysis tools.
The Master node can sense a wide(r) variety of conditions such as snow pack presence.
Calibration: use reference instruments including a portable soil temperature and moisture measurement device.

## Slide 9: Sensor Network: Topology
Master/Sensor star topology
Sensor nodes
  Collect data (temperature, soil moisture, etc.)
  Use LoRa radio to send data to Master
Master
  Receives data from sensors using LoRa
  Forward data to ‘Application Server’ via Internet
Internet
Sensor node
Master node

## Slide 10
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors sleep most of the time to conserve power

## Slide 11
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors wake up and measure environmental parameters

## Slide 12
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors transmit data to the Master

## Slide 13
Internet
Sensor node
Master node
Sensor Network: Operation
Sensors go back to sleep

## Slide 14
Internet
Sensor node
Master node
Sensor Network: Operation
The Master node forwards the collected data to an Application Server in the Internet

## Slide 15
Internet
Sensor node
Master node
Sensor Network: Operation
The Master returns to its nominal mode

## Slide 16: Overview
About Open Source Hardware
Our designs for an in-situ sensor network
LoRa Background
Test implementation

## Slide 17: Test Implementation – Master Node
Design work started in Fall 2019 by Mtech Students with faculty mentor
Designed to function standalone
Satellite module for connection to the Internet
MCU/RTC to control power
3.3Ah/year power requirement*
Add LoRa for Sensor Nodes
*Apple 2019 laptop has a 4.5Ah battery

## Slide 18: Test Implementation – Sensor Node
Sensor node
  LoRa + Arduino + Temperature and soil moisture sensor
  LiMnO2 batteries (-50° C)
  Prototypes operated at -25°C and were run buried in both soil and snow as well as in open air
  Total parts cost < $50; options exist to reduce that cost further
  Dropped MCU sleep in favor of a power latch
  Estimated 1 Ah/year power requirement @ 3.0v
Design info:
  github.com/jgallagher59701/Soil_moisture

## Slide 19: Implementation Notes
Satellite uplink chosen by Mtech Master Node developers to broaden deployment locations (over cell technology)
Both the Mtech and OPeNDAP developers independently decided on ‘power latch’ technique to control power consumption, esp. the power used by the communication technology
  A better option than the peripheral’s sleep modes
  The Master Node design uses a second MCU to toggle power (using a built in clock).
  The Sensor Nodes uses discreet components in combination with a real-time clock
Master/Sensor LoRa protocol
  Reliable Datagram – was previously an ad hoc protocol – concerns regarding collisions
Application Server
  CHORDS or ERDDAP server running on Amazon Web Services EC2 instance

## Slide 20: Questions?

## Slide 21: Bonus material on LoRa

## Slide 22: Overview
About Open Source Hardware
Our designs for an in-situ sensor network
LoRa Background
Test implementation

## Slide 23: LoRa Background: What is LoRa?
“LoRa (short for Long Range) is a spread spectrum modulation technique derived from chirp spread spectrum (CSS) technology.”*
Spread Spectrum: To spread an information signal over a (wide) band of radio frequencies.
Robust transmission technique; also used in WiFi, Cell phones, Bluetooth, etc.
Hedy Lamarr and George Antheil are credited with its invention
*https://www.semtech.com/lora/what-is-lora
Antheil2
Lamarr1
Notes: 1 By Unknown - eBay, Public Domain, https://commons.wikimedia.org/w/index.php?curid=47176716
2 By unknown - picture found at http://www.schirmer.com/default.aspx?TabId=2419&State_2872=2&ComposerId_2872=35, Fair use, https://en.wikipedia.org/w/index.php?curid=23450183

## Slide 24: LoRa specifics
Widespread use by Internet of Things applications.
Inexpensive (~$5 eBay; $20 Adafruit/SparkFun)
Small (16mm x 16mm)
Range: 1–10km
Adjustable bit rate: 293 bps to 37.5 kbps
Adjustable error correction, etc., parameters
Works well with Arduino and similar MCUs
Good library support (e.g., RadioHead; TinyLora)
US/EU/AS frequency bands (915/868/430 MHz)
Low power – 20mA receive/100mA transmit
Image from the SparkFun website

## Slide 25: How LoRaWAN Relates to LoRa
Network layer defined by the LoRa Alliance
Physical layer defined by the radio hardware
Physical Layer
Network Layer

## Slide 26: Alternatives to LoRaWAN: LoRa Physical link
MCU software library: RadioHead.2
  We’re using RadioHead, but there are other libraries for LoRa.
How the physical link can be configured
  Power level (5 to 23 dBm), Bandwidth, Coding rate, Chips/symbol, CRC3
  The last four determine data rate and noise rejection
  Supports hardware Channel Activity Detection (CAD)
Using the SPI bus
  Many LoRa boards use the SPI bus and signal reads and writes using interrupts
  If there are other SPI-based devices, disable interrupts while using another device
  Other SPI devices include SD memory cards
2. http://www.airspayce.com/mikem/arduino/RadioHead/; or https://github.com/adafruit/RadioHead
3. https://en.wikipedia.org/wiki/Cyclic_redundancy_check

## Slide 27: RadioHead Architecture
Driver + Manager: Implements the physical and logical network layers
Driver
  C++ object that supports a particular transceiver
  Can be used alone, without a Manager
  Suitable for early prototypes and/or very simple uses
  Various Drivers support different max packet sizes (28 to 255 octets)
  RFM95W  251 octets (i.e., HopeRF and Semtech LoRa boards)
Manager
  C++ object that uses a Driver to implement a logical network
  Objects exist for Datagram, Reliable Datagram, Router and Mesh protocols

## Slide 28: RadioHead Manager Classes
These are based on well-known networking principles
Addressing: Assigning an address to each device helps maintain reliability when scaling up a network to more nodes
Datagram:
  A simple addressed protocol. Every packet has an 8-bit SRC and DEST address
  Also supports a Broadcast ‘address’ (0xFF)
  No error detection
Reliable Datagram:
  Addressing + simple error recovery: messages are acknowledged by the recipient, and unacknowledged messages are retransmitted until acknowledged or the retries are exhausted
  Broadcast does not support error detection

## Slide 29: Routing and Meshes
RHRouter enables multi-hop transmissions
  LoRa networks can be designed to move information between star nodes
  Must be deployed with care since intermediate nodes will need more power
  Can support larger topological deployments with fewer Internet uplink sites
  Routing tables must be manually managed in software (using 8-bit addresses)
RHMesh enables automatic route discovery
  This supports dynamically adding and removing both leaf and internal nodes
Router and Mesh are useful for the ’star’ node in our design, but not for the leaf nodes, which will be powered down for all but the few seconds they sample and transmit data.

## Slide 30: Generic IoT/LoRa Topology
Autonomous sensors communicate with LoRa Gateways
LoRa Gateways transfer information to the Internet
Once on the Internet the information can be routed to data servers, etc.
This can use LoRaWAN (a kind of Low Power Wide Area Network – LPWAN) or Datagrams
Picture: Semtech1
Notes: 1https://www.semtech.com/lora/what-is-lora

## Slide 31: More information
What is LoRa, Semtech website: https://www.semtech.com/lora/what-is-lora
Comparison of LoRa with FSK (frequency Scaled Keying): Jesus Sanchez-Gomez, Ramon Sanchez-Iborra, and Antonio Skarmeta, Transmission Technologies Comparison for IoT Communications in Smart-Cities. 2017. DOI: 10.1109/GLOCOM.2017.8254530.
The Things Network (non-profit) : https://www.thethingsnetwork.org/
MathWorks ThingSpeak: https://thingspeak.com/
LoRa Alliance (non-profit) – LoRaWAN information source: https://lora-alliance.org/
LoRa Datagram open source implementation: https://www.airspayce.com/mikem/arduino/RadioHead/classRHReliableDatagram.html
LoRaWAN open source implementation: https://github.com/adafruit/TinyLoRa
RadioHead library: http://www.airspayce.com/mikem/arduino/RadioHead/; or https://github.com/adafruit/RadioHead